## Slide 1: NYC Town & Gown: Climate Vulnerability, Impact, and Adaptation Analysis (VIA)
Characterizing current and future extreme heavy rainfall in NYC
Franco Montalto and Bernice Rosenzweig (Task Co-Leads), Art DeGaetano, Colin Evans, Mobin Rahimi-Golkhandan, Patrick Gurian, Radley Horton, Joel Kaatz, Jerry Kleyman,
Rachel Lo, Philip Orton, Fernando Pasquel, Matina Shakya

## Slide 2: Agenda
The use of precipitation information in New York City operations and planning
Observations of Historic Heavy Rain
Observed trends in subdaily precipitation in New York City: Results of nonparametric approach
Observed trends in subdaily precipitation in New York City: Results of parametric approach
Clausius Clapeyron scaling
Delta change factors

## Slide 3: Stakeholders
Precipitation Information

## Slide 4: Information Flows

## Slide 5: Observations of historic heavy rain

## Slide 6: Rainfall Observation Sites (> 50-years of data)
New York City
KNYC: Central Park
KLGA: LaGuardia International Airport
KJFK: John F. Kennedy International Airport
NYC area
KEWR: Newark Liberty International Airport, NJ
KBDR: Sikorsky Airport, CT
Closest to Municipal Reservoir Watersheds
KALB: Albany International Airport

## Slide 7: Highest Observed Hourly Rainfall (1950-2022)
Rank | Newark Liberty Airport (KEWR) |  | Central Park (KNYC) |  | LaGuardia Airport (KLGA) |  | Kennedy Airport (KJFK) | 
 | Time (EST) | Precip (in.) | Time (EST) | Precip (in.) | Time (EST) | Precip (in.) | Time (EST) | Precip (in.)
1 | 9/1/21 19:00 | 3.62 | 9/1/21 20:00 | 3.47 | 9/1/21 20:00 | 2.8 | 7/31/96 11:00 | 2.88
2 | 7/21/06 16:00 | 2.63 | 7/17/95 23:00 | 1.95 | 7/15/97 19:00 | 2.44 | 6/30/84 12:00 | 2.45
3 | 8/17/74 17:00 | 2.04 | 8/10/06 19:00 | 1.9 | 8/17/98 14:00 | 2.09 | 8/14/11 4:00 | 2.41
4 | 7/17/95 23:00 | 2.00 | 8/21/21 22:00 | 1.84 | 11/4/50 23:00 | 1.97 | 6/30/84 11:00 | 2.15
5 | 5/27/91 23:00 | 1.95 | 9/8/04 7:00 | 1.76 | 7/17/95 23:00 | 1.97 | 8/8/07 6:00 | 2.04
6 | 8/4/03 15:00 | 1.92 | 6/3/91 22:00 | 1.75 | 8/8/07 6:00 | 1.87 | 8/28/83 21:00 | 1.88
7 | 8/8/07 5:00 | 1.82 | 8/14/05 19:00 | 1.7 | 7/6/75 17:00 | 1.83 | 8/20/91 16:00 | 1.84
Key Messages:
Of the top 7 hourly accumulations, only 3 were ranked at the top for more than one station
Hourly rainfall extremes are highly localized

## Slide 8: Time Series of National Weather Service Flooding Episodes
Key Messages:
There have been many impactful flooding events in NYC since 1986
Transit disruptions are the most common reported impact

## Slide 9: Comparison of Observed Hourly Rainfall (1950-2022) with Historical Flooding Episodes
Rank | Newark Liberty Airport (KEWR) |  | Central Park (KNYC) |  | LaGuardia Airport (KLGA) |  | Kennedy Airport (KJFK) | 
 | Time (EST) | Precip (in.) | Time (EST) | Precip (in.) | Time (EST) | Precip (in.) | Time (EST) | Precip (in.)
1 | 9/1/21 19:00 | 3.62 | 9/1/21 20:00 | 3.47 | 9/1/21 20:00 | 2.8 | 7/31/96 11:00 | 2.88
2 | 7/21/06 16:00 | 2.63 | 7/17/95 23:00 | 1.95 | 7/15/97 19:00 | 2.44 | 6/30/84 12:00* | 2.45
3 | 8/17/74 17:00 | 2.04 | 8/10/06 19:00 | 1.9 | 8/17/98 14:00 | 2.09 | 8/14/11 4:00 | 2.41
4 | 7/17/95 23:00 | 2.00 | 8/21/21 22:00 | 1.84 | 11/4/50 23:00 | 1.97 | 6/30/84 11:00 | 2.15
5 | 5/27/91 23:00 | 1.95 | 9/8/04 7:00 | 1.76 | 7/17/95 23:00 | 1.97 | 8/8/07 6:00 | 2.04
6 | 8/4/03 15:00 | 1.92 | 6/3/91 22:00 | 1.75 | 8/8/07 6:00 | 1.87 | 8/28/83 21:00 | 1.88
7 | 8/8/07 5:00 | 1.82 | 8/14/05 19:00 | 1.7 | 7/6/75 17:00 | 1.83 | 8/20/91 16:00 | 1.84
NWS flood or flash flood episode
Pre-1986
Key Messages:
Most of the top 7 hourly accumulations triggered floods and occurred since 1986

## Slide 10: Evaluation of historical trends in precipitation observations
Key considerations
Availability of quality controlled data
  Duration of uninterrupted record
  Sampling frequency
Sampling variability
  Accumulation/intensity over sampling interval (e.g. hourly)
  Accumulation/intensity over prescribed time clusters (e.g. 24-hour calendar day)
  Accumulation/intensity within an event, defined with a specific separation period
Approach to statistical analysis
  Non-parametric methods
  Parametric methods

## Slide 11: Evaluation of historical trends in precipitation observations
Nonparametric Approach
Utilizes discrete rain events (defined using a 4-hour interevent dry period)
  Set #1: All events (1955-2022)
  Sets #2 and #3: Events exceeding 95th and 99th percentile thresholds
For each set, we focused on four event attributes, and their frequencies
  Total accumulation
  Total duration
  Peak hourly intensity
  Average intensity
This approach does not assume any statistical distribution of the data, and is thus less sensitive and less likely to detect trends

## Slide 12: Evaluation of historical trends in precipitation observations
Parametric Approach
Fits a Generalized Extreme Value (GEV) distribution to a Partial Duration Series (PDS)
  Different PDS generated for precipitation accumulations over 1- 24 hr time clusters
Subject to tail variability
  Can be heavily influenced by one or more extreme events (e.g. Post Tropical Cyclone Ida in Central Park)
Represents the classical methodology for developing IDF curves

## Slide 13: Precipitation event characteristics

## Slide 14: Total Event Precipitation

## Slide 15: Peak Hourly Intensity

## Slide 16: Event Average Intensity

## Slide 17: Event Duration

## Slide 18: Evaluation of historical trends in precipitation observations: Nonparametric findings

## Slide 19: Key Messages from the Nonparametric approach
Annual precip and event precipitation (all events) are increasing at all NYC gauges
Events with >95th percentile average and peak hourly intensities are getting more frequent at all NYC gauges
  Could be due to a statistically significant shortening of event durations at some locations
Events with > 95th percentile event totals are getting more frequent at KEWR and KNYC
Extreme events do not seem to be getting larger, more intense, or longer

## Slide 20: Evaluation of historical trends in precipitation observations: Parametric findings
Key Messages (Central Park):
We observed increases in the 2-, 5-, 10-, 25-, 50-, and 100-yr extreme rainfall events for durations of 1-hr through 24-hours at all stations, when the analyzed record includes data after 1990
There is a consistent pattern of increasing percent change for higher return periods
We see a decrease in percent change with precipitation duration
Increase is not smooth but influenced by specific events

## Slide 21: Evaluation of historical trends in precipitation observations: Parametric findings
Key Messages (Central Park):
Comparing early and late periods, we see smaller differences with longer durations
Some of the changes exceed the confidence interval, but this finding is inconsistent across stations

## Slide 22: Evaluation of historical trends in precipitation observations: Parametric findings

## Slide 23: Key Messages from the Parametric approach
At Central Park, the 2-year return period for 1-hour precipitation totals has increased by roughly 5% since 1950
Hourly precipitation totals have increased at a greater rate than daily totals during the latter half of the observational record, but this is not reflected across the larger region and it is not reflected in modeled data
Since 2000, the maximum percentage of the 24-hour PDS case rainfall totals that fell during one hour has increased.
Approximately 23% of the 1-hour PDS case rainfalls are also part of a 24-hour PDS case. There has been little change in this percentage across the period of record.

## Slide 24: Clausius-Clapeyron Scaling - Methods
Goal: Check if hourly precipitation increases with dry buld and dew point temperature per thermodynamic relationships (6-7% / degree C)
Methods:
  Conducted using hourly data at 4 regional gauges
    Non-zero precipitation hours with dry bulb and dewpoint temperature
  Analyzed 90th, 95th, and 99th percentile precipitation quantities for 2C bins
  Produced relative frequency plots
  Produced log-transformed precipitation vs temperature plots
    Added lines depicting CC relationship for reference

## Slide 25: Clausius-Clapeyron Scaling - Temporal Distribution
Key Messages:
Most of the extreme events occurred between 20-22 C (all stations)

## Slide 26: Clausius-Clapeyron Scaling - Dry-bulb Temperature
Key Messages:
Abrupt decline in slope after 20-24 C, attributed to the lesser number of low-probability extreme events at higher temperatures
No major differences between more distant and more recent past

## Slide 27: Clausius-Clapeyron Scaling - Dewpoint Temperature
Key Messages:
The curves representing more extreme precipitation (e.g., 99th percentile) follow the CC relationship more closely than the curves representing the less extreme precipitation

## Slide 28: Expected Future Changes in Extreme Precipitation

## Slide 29: Delta Change Factors
Represent the change signal between the historic and future period in climate projections
Computed based on the quantile delta method (QDM)

## Slide 30: Delta Change Factors (low emissions SSP245)
Early (2020-2069)
Late (2050-2099)
SSP245 EARLY: | 2020-2069 |  |  |  |  | 
PERCENTILE | 2-yr | 5-yr | 10-yr | 25-yr | 50-yr | 100-yr
10th | 1.04 | 1.02 | 0.97 | 0.85 | 0.84 | 0.84
25th | 1.09 | 1.07 | 1.08 | 1.02 | 0.94 | 0.95
Mean | 1.16 | 1.20 | 1.19 | 1.16 | 1.14 | 1.17
75th | 1.20 | 1.27 | 1.25 | 1.27 | 1.29 | 1.29
83rd | 1.26 | 1.35 | 1.34 | 1.37 | 1.35 | 1.39
90th | 1.32 | 1.44 | 1.44 | 1.46 | 1.44 | 1.58
SSP245 LATE: | 2050-2099 |  |  |  |  | 
PERCENTILE | 2-yr | 5-yr | 10-yr | 25-yr | 50-yr | 100-yr
10th | 1.08 | 1.08 | 1.04 | 0.91 | 0.88 | 0.87
25th | 1.14 | 1.14 | 1.14 | 1.06 | 1.03 | 1.05
Mean | 1.22 | 1.28 | 1.28 | 1.23 | 1.24 | 1.26
75th | 1.28 | 1.40 | 1.37 | 1.35 | 1.36 | 1.40
83rd | 1.31 | 1.44 | 1.51 | 1.45 | 1.43 | 1.52
90th | 1.34 | 1.47 | 1.61 | 1.58 | 1.56 | 1.64

## Slide 31: Delta Change Factors (high emissions SSP585)
SSP585 EARLY: | 2020-2069 |  |  |  |  | 
PERCENTILE | 2-yr | 5-yr | 10-yr | 25-yr | 50-yr | 100-yr
10th | 1.04 | 1.00 | 0.93 | 0.82 | 0.79 | 0.84
25th | 1.11 | 1.08 | 1.09 | 1.02 | 1.06 | 0.98
Mean | 1.18 | 1.21 | 1.23 | 1.18 | 1.21 | 1.23
75th | 1.24 | 1.27 | 1.39 | 1.34 | 1.42 | 1.44
83rd | 1.27 | 1.35 | 1.42 | 1.40 | 1.46 | 1.53
90th | 1.35 | 1.46 | 1.45 | 1.43 | 1.52 | 1.64
SSP585 LATE: | 2050-2099 |  |  |  |  | 
PERCENTILE | 2-yr | 5-yr | 10-yr | 25-yr | 50-yr | 100-yr
10th | 1.15 | 1.09 | 1.07 | 1.01 | 0.97 | 0.93
25th | 1.18 | 1.17 | 1.16 | 1.09 | 1.07 | 1.05
Mean | 1.28 | 1.32 | 1.35 | 1.32 | 1.30 | 1.30
75th | 1.39 | 1.46 | 1.59 | 1.53 | 1.47 | 1.56
83rd | 1.41 | 1.55 | 1.61 | 1.58 | 1.59 | 1.63
90th | 1.45 | 1.59 | 1.64 | 1.67 | 1.68 | 1.75
Early (2020-2069)
Late (2050-2099)

## Slide 32: General Recommendations
Increase the spatial density of high temporal frequency precip gauges
Invest resources to centralize, quality control, warehouse, develop procedures to maintain and facilitate access to precipitation data for general accessibility and policy updates
Climate model projections constantly show increases in future design storms of 15-30 percent. Such changes should be factored into storm water design guidance.
More research needed in the types of weather systems responsible for different rainfall intensities

## Slide 33: Thanks!
For follow up contact Dr. Franco Montalto, P.E. at fam26@drexel.edu