## Slide 1: Utilidor project – Report
Alec Tristani, Chloé Arson
Wednesday, January 14th 2026
Based on the work of 13 motivated undergraduate and graduate students:
Royce Andrews, Junwon Hur, Yiksan Yu, Qinghe Xu, Tanvi Saxena, Ivy Quan, Matthew Zhang, Karen Chen, Andy Chen, Annelise Gross, Caroline Schell, Fatima Bah and Ian Grenda

## Slide 2: Why utilidors?
Hand Excavation to expose the Interfering Telecom and Electrical Utilities Overlying the New Water Main Alignment
Exposed Telecom and Electrical Utilities with the start of Casing Removal
Benefits of utilidors:
Eﬀective use of ground level surface;
Long-term management, accessibility and productivity;
Less prone to wear and tear;
Long-term outlook outweighs the short-term costs.

## Slide 3: New York City traffic statistics
Highest traffic delay times by city – Worldwide (2024)

## Slide 4: Short-term project: optimize utilidor designs
Conduct a scientific literature review on utilidors worldwide and on the geology of New York City.
Perform 2D numerical simulations to evaluate structural stability under different geotechnical configurations
Analyze tunnel cross-section shapes: assess geometry, lining thickness & dimensional requirements
Provide design recommendations for the construction of utilidors across the city
Confined Space Access into a Utilidor
Utilidor compartmentalization for access and security – Cross Section of Marina Bay Utility Tunnel
Objective: Design utilidors

## Slide 5: Utilidors in the world
Helsinki, Finland:
200 km of technical/maintenance, of which 60km dedicated to heating, cooling and electricity.
Located 20 m to 120 m below ground level
Currently existing utilidors in China with square and circular cross-sectional shapes.
Beijing, Shanghai, China (Multi-Utility-Tunnels):
Shallow depth (3 m), large dimensions (> 6 m)
Rectangular and Circular cross sections
Objective: Conduct a literature review to examine current worldwide practices in utilidor design.

## Slide 6: NYC Geology
Rock Properties in New-York City
Objective: Characterize the ground properties to enable accurate numerical simulations.

## Slide 7: Numerical Modeling – Problem Setup
Objective: Perform 2D numerical simulations to evaluate structural stability under different geotechnical configurations.

## Slide 8: Parametric studies – Comparison with analytical solutions
Bobet and Einstein, “Tunnel Design Methods” Fig 4.6

## Slide 9: Parametric studies – Section shape and depth
Manhattan Schist parameters
Young’s modulus - E = 1.5 x 1010 Pa
Poisson’s ratio = 0.3
(coeﬀ. of earth pressure) K = 1
Unit weight - γ = 1.8 x 104 N/m3

## Slide 10: Parametric studies – Effects of depth, section shape and elastic parameters
Chart: Tangential Stress as a Function of Depth
| 3 | 3.5 | 4 | 4.5 | 5 | 5.5
stt | 2136990 | 2455530 | 2856630 | 3165670 | 3501150 | 3835800
Chart: Tangential Stress as a Function of Poisson's Ratio
| 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4
stt | 2318100 | 2277000 | 2230000 | 2185610 | 2136990 | 2102970 | 2093440

## Slide 11: Parametric studies – Effect of the support and sequential excavation
Portland cement
E = 20 GPa
Poisson’s ratio = 0.2
Density = 2,400 kg/m3 (American Shotcrete Assoc.)

## Slide 12: Conclusions and future work
Pedagogic conclusions:
Students were able to learn new concepts related to geotechnical engineering and tunnel design
Research skills: scientific literature review, self-learning, independence
Multidisciplinary work: geomechanics theory, infrastructure design, numerical modeling, scientific visualization
Technical conclusions:
Square cross section shapes at shallow depth and circular section for deeper tunnels
Recommend NYC include depth of tunnel/overburden pressure as important parameter
Future work:
Consider groundwater behavior, heterogeneities and account for plasticity
Complexify the geometry and account for side corridors
Extend the study to other areas besides Manhattan
Develop a tool readily applicable by practitioners based on machine learning

## Slide 13: Long-term project: develop predictive maintenance tools
 Identify data sources that will be collected in practice
Generate synthetic data when necessary using analytical or numerical methods
Construct a virtual model, whether based on analytical or numerical approaches
Integrate data into the virtual model to complete a Digital Twin
Explore the use of machine learning techniques to enhance Digital Twin implementation
Typical congested condition at site of utility construction (Right) and close-up view exposed underground utilities (left)
Objective: improve current maintenance operation systems

## Slide 14
Utilidor project – Report
Urban Engineering – Shallow tunnels – Rock Mechanics – Numerical modeling – Data Analysis – Predictive maintenance
Thank you for your attention!
Contact:
Chloé Arson: cfa36@cornell.edu
Alec Tristani: ayt34@cornell.edu