## Slide 1
Pilot-Plant Design for
Biomass Pyrolysis
Che391 Pilot-Plant Design for Biomass Pyrolysis
Sungone Philip Seo

## Slide 2
Project Purpose
Vendors
PYREG
ETIA Ecotechnologies
Bioforcetech
Pyrocal
Airburners
Operators
Quonset Soil Solutions
Standard Biochar
Ephrata Borough Authority
Downer
Customers
Biochar Price

## Slide 3
Auger vs. Hearth
Auger Reactor
Hearth Reactor
Biomass is moved by a rotating screw
Tightly sealed
Biomass is moved by gravity
Mechanically simpler but larger

## Slide 4
Vendor 1: PYREG
Country
Germany
2009
Founded
Installed over 50 plants and EBC type-certified (European Biochar Certificate)
Portfolio
Rhineland-Palatinate, Germany
HQ
PX500, PX1500, PX6000
Product
Auger
Reactor
https://pyreg.com/
Company based in Germany making biomass and biosolids pyrolizers

## Slide 5
3 products
Products PX500/1500/6000
Product Specifications
Specifications | PX500 | PX1500 | PX6000
Footprint | 12m*6m*5m | 13m*7m*7.8m | 21m*14m*7.5m
Temperature | 500~700 °C |  | 
Feedstock | Hay, wood chips, nut shells, cardboard, etc |  | 
Capacity | 0.15t/h | 0.4125t/h | 1.65t/h
Power Consumption (Max) | 12kW (E) | 38kW (E) | 120kW (E)
Heat Output | 200kW (Q) | 600kW (Q) | 2,500kW (Q)
Remark | Has testing center for personal analysis |  | 

## Slide 6
Vendor 2: ETIA
Country
France (became part of Norwegian group in 2019)
1989 (First biochar plant in 2016)
French engineering group that provides tailor-made electrically heated reactors
Founded
150 delivered machines in 35 countries (Including U.S)
Portfolio
Paris
HQ
Biogreen (electrically heated screw conveyor)
Product
Auger-based
Reactor
https://etia-group.com/

## Slide 7
Electrically heated screw conveyor
Product Biogreen
Spirajoule Specifications
Specifications | 
Footprint | Tailor-made solutions
Temperature | ~850 °C
Feedstock | Any kind of non-ferrous dry material (Mostly biomass, plastics, waste)
Capacity | ~1t/h
Remark | Heated by low voltage current
 | Residence time can be controlled by screw rotation speed
 | Easy and reliable control of temperature/residence time

## Slide 8
Vendor 3: BIOFORCETECH
Country
U.S
2012
Founded
Installed 14 plants in US and Italy
Portfolio
San Francisco
HQ
Sigma
Product
Auger
Reactor
https://bioforcetech.com/
Based in San Francisco. All completed projects are based on biosolid pyrolysis

## Slide 9
Product Sigma
Sigma Specifications
Specifications | Sigma
Footprint | 11m*2.9m*2.9m
Temperature | 500~700 °C
Residence Time | 10-30 minutes
Empty Weight | 13,500Kg
Feedstock | Biosolids, sewage sludge, wood chips, nut shells, manure (Particle size: ~30mm; Moisture: 5-35%)
Capacity | ~0.11t/h
Remark | Destroys PFAS

## Slide 10
Vendor 4: PYROCAL
Country
Australia
2014
Founded
Around 20 units in 8 countries
Portfolio
Toowoomba, Australia
HQ
CCT12, CCT20
Product
Remark
https://www.pyrocal.com.au/
Hearth-based reactor
Based in Australia, hearth-based reactors

## Slide 11
Product CCT12/CCT20
Specifications
Specifications | CCT12 | CCT20
Footprint | 15m*4m*5m | 32m*14m*9m
Temperature | - | 
Feedstock | Biomass, biosolids (Moisture: ~12%; Particle Size: 10mm*10mm) | 
Capacity | 0.2t/h | 0.6t/h
Power Consumption | 15~30kW (E) | 40~60kW (E)
Heat Output (Max) | 480kW (Q) | 1440kW (Q)
Remark | Has testing center for personal analysis | 

## Slide 12
Vendor 5: Air Burners
Country
United States
1997
Founded
30+ international markets
Portfolio
Palm City, Florida
HQ
FireBox Series
Product
Reactor
Air Curtain Burner
Portable “closed circle recycling” technology for on-site biomass disposal

## Slide 13
Vendors & Products
Specifications
Vendors | Product | Volume | Temperature | Feedstock | Capacity | Electricity Consumption | Heat Output
ETIA (France) | Biogreen | - | ~ 850 °C | Biomass, Biosolids | 1t/h | - | -
PYREG (Germany) | PX500 | 360 m³ | 500~700 °C |  | 0.15t/h | 12kW | 200kW
 | PX1500 | 710 m³ |  |  | 0.4125t/h | 38kW | 600kW
 | PX6000 | 2205 m³ |  |  | 1.65t/h | 120kW | 2,500kW
BIOFORCETECH (San Francisco) | Sigma | 92.5 m³ | 500~700 °C |  | 0.11t/h | - | -
PYROCAL (Austrailia) | CCT12 | 300 m³ | 500~700 °C |  | 0.2t/h | 15~30kW | 480kW
 | CCT20 | 4032 m³ |  |  | 0.6t/h | 40~60kW | 1,440kW
Air Burners (Florida) | FireBox S100 | 44 m³ | ~ 1000 °C | Biomass | 3-5t/h | - | -
 | FireBox S200 | 69 m³ |  |  | 7-9t/h |  | 
 | FireBox S300 | 128 m³ |  |  | 11-13t/h |  | 
Average Electricity Consumption:
88kW (for 1t/h capacity)
Average Heat Output:
1820kW (for 1t/h capacity)
Average Volume:
2420 m³ (for 1t/h capacity)
Airburners’ main focus is on making portable reactors for disposing biomass through controlled burning
Average Temperature:
620 °C

## Slide 14
Operator 1: Standard Biocarbon
Vendor
PYREG
2020
4 PYREG units operating in Maine using residual wood from Lumber Production (Pleasant River Lumber)
4.3 million tons of low-grade wood demand disappeared since 2014
Founded
$5.6 Million
Project Cost
Portland, Maine
HQ
Residual wood product from lumber production
Feedstock
4 units of PX1500
Units
2022
Startup

## Slide 15
Operator 2: Quonset Soil Solutions
Vendor
ETIA
2023
4 operating units from ETIA in Rhode Island using forest by-products to produce 6,000 ton/year biochar
Founded
$27 Million
Project Cost
Cranston, Rhode Island
HQ
Forest by-products
Feedstock
4 Biogreen Reactors
Units
2025
Startup
https://qssbiochar.com/our-products/

## Slide 16
Operator: Public Agencies
Vendor
Bioforcetech (Dryers), PYREG (Pyrolizers)
Ephrata, Pennsylvania
Location
Not Public
Project Cost
Dewatered biosolids (wastewater treatment)
Feedstock
2025
Startup
Vendor
BluSkyCarbon Inc.
Minneapolis
Location
Not Public
Project Cost
Urban wood waste
Feedstock
2025
Startup

## Slide 17
Pyrolizers in Use
Specifications
Vendors | Product | Operator | Project |  |  |  | 
 |  |  | Project Cost | Business Type | Feedstock | Feedstock Consumption | Startup
ETIA (France) | Spirajoule | Quonset Soil Solutions (Rhode Island) | $27 Million | Private | Biomass | 35,000 ton/year (Estimated) | 2025
PYREG (Germany) | PX500 | Standard Biochar (Maine) | $5.6 Million | Private | Biomass | 12,000 ton/year | 2022
 | PX1500 |  |  |  |  |  | 
 | PX6000 |  |  |  |  |  | 
BIOFORCETECH (San Francisco) | Sigma | Ephrata Borough Authority (Pennsylvania) | - | Public | Biosolids | 4,000 ton/year | 2025
BluSkyCarbon (Canada) | Vulcan II | Minneapolis City | - | Public | Biomass | 3,600 ton/year | 2025
Project Cost per 1,000 ton/year:
$620,000

## Slide 18
Biochar Price
Systematic review on biochar price (published 2023)
Campion, N.; Sproul, E.; Oates, L.; Krapf, M.; Yamaji, K.; Yeo, J.-Y.; McElroy, E. E.; Ingraffia, M.; Davidson, M. R.; Kohler, H.-P. E.; et al. Techno-Economic, Environmental and Social Assessments of Biochar Systems: A Systematic Review. J. Clean. Prod. 2023, 405, 136296.
median
Range
$17.15
~
$2,710 (per ton)
Median
$400

## Slide 19
Future Work
  Better Economic Analysis
  Optimization
  Process Simulation

## Slide 20
Thank you