## Slide 1: Subsurface Engineering with 2075 In Mind – A UK Perspective
Professor Chris Rogers University of Birmingham
Resilience Through Innovation Critical Local Transport and Utility Infrastructure

## Slide 2: Streets and the Urban Metabolism
The urban metabolism – the flows facilitating urban living:
People in vehicles
Access to public transport
Active travel
Goods delivery
Frontages to residences
Dwell spaces, place-making
Access to nature, flora …
… and fauna – biodiversity
Ventilation, pollination
Buried utility services
… water, gas, electricity, wastewater, data, ideas
Image credit: Dr Mike Farrimond, UKWIR
Tree
Roots ?
The veins and arteries supporting societies

## Slide 3
Expert reviews
Scenarios & visions
Analytics
Future trends analysis
6 dimensions of future cities were explored
LIVING
ECONOMY
ENVIRONMENT
FORM
INFRASTRUCTURE
GOVERNANCE

## Slide 4
Expert reviews
Scenarios & visions
Analytics
Future trends analysis
LIVING
ECONOMY
ENVIRONMENT
FORM
INFRASTRUCTURE
GOVERNANCE
For comprehensive evidence, we considered diverse methods, from multiple disciplines
All city systems are interdependent
to some degree … intervene in one
system and others are impacted to
a greater or lesser degree

## Slide 5: Urban Underground Space Planning
The subsurface has been described as:
“the final urban frontier waiting to be exploited by those who place the first stake and thereby claim their space” (Admiraal and Cornaro, 2016)
There are international exemplars of good practice:
  The Netherlands aims to create a uniform and detailed register of subsurface data
  Helsinki was the first city in the world to create an Underground Masterplan (in 2009)
  Space-constrained Singapore has a 3D Special Detailed Control Plan
And in the UK we have launched the
  National Underground Assets Register (NUAR)
  … following NETTWORK, Mapping the Underworld, and a UK Geospatial Commission

## Slide 6: National Underground Assets Register
  The National Underground Assets Register (NUAR)
  … is a security-protected digital platform for sharing data on of buried pipes and cables
  … along with geology, groundwater and other subsurface features
  … should be an integrator of disparate datasets held in disparate places
… enables ‘digital twins’ to simulate the impacts of subsurface interventions
… fosters coordination and collaboration – joineduppedness features in systems thinking
  The UK Government’s Foresight Future of the Subsurface embraces a broader perspective
  … calls for subsurface planning to be as rigorous as surface planning
  … planning should be truly 3D, rather that 2D on the ground surface looking upwards
  … the shallow subsurface is a complex, congested space and requires systemic practices
  … synergistic systemic practices must extend to regulation – and all forms of governance

## Slide 7: Roles and Responsibilities
This leads to some fundamental questions:
  Who is responsible for looking after the urban subsurface, and for whom?
  What all the many and varied potential outcomes that we could achieve via our subsurface engineering?
Adapting Brundtland’s (1987) definition of sustainability …
“subsurface engineers should engineer to meet the needs of today without compromising the ability of future subsurface engineers to meet their own needs”.
This is not (just) for sustainability and resilience – some might say “nice to have” – but
… because it make good business sense

## Slide 8: What is a Theory of Change?
A theory of change is a methodology that identifies outcomes that are needed and wanted
… and works out what must happen to deliver the outcomes

## Slide 9
Example of a system map to identify system interdependencies
… and all stakeholders who influence or are influenced by an intervention in the system of interest
… and from which current (baseline) performance of the system of interest can be deduced
… and the current problems can be (fully) identified
Map created by Chris Bouch
University of Birmingham

## Slide 10
Map created by Chris Bouch
University of Birmingham
For each design option for a system intervention, the map helps
… identify the likely consequences of its implementation
… identify all potential forms of value creation
… hence formulate the alternative business models associated with each design option
This serves to
… deliver the widest possible range of value from the system intervention
… de-risk the investment by
making transparent all the likely consequences of implementation

## Slide 11: Assessing the Underworld’s Core Proposition
... if the ground properties change, or the ground moves, the adjacent / overlying infrastructure responds accordingly
When creating, maintaining, upgrading or repurposing buried infrastructure
... we need to be informed by the ground conditions and how the ground might react to any new activity or intervention
Before we engineer in the underworld, we need to
This treats the ground as an infrastructure in its own right
… with performance criteria and deterioration models
… assess the condition of buried infrastructure
… assess the condition of the ground in which it is buried
… assess the condition of the road that overlies it
What is buried in, and on, the ground is controlled by the ground

## Slide 12: Streets and the Urban Metabolism
The urban metabolism – the flows facilitating urban living:
People in vehicles
Access to public transport
Active travel
Goods delivery
Frontages to residences
Dwell spaces, place-making
Access to nature, flora …
… and fauna – biodiversity
Ventilation, pollination
Buried utility services
… water, gas, electricity, wastewater, data, ideas
Image credit: Dr Mike Farrimond, UKWIR
Tree
Roots ?
The veins and arteries supporting societies

## Slide 13: Maintaining & Repairing Buried Infrastructure in the Urban Subsurface

## Slide 14: Installing Buried Infrastructure in the Urban Subsurface

## Slide 15: Remember our Raison D’Etre
  Buried infrastructure – supports civilised life, facilitates ‘urban systems’
  Buried infrastructure – provides resources, enables things to move unrestricted
  Buried infrastructure … is there for people and society – the ultimate clients?
  What do people want?
  Hence – efficient and effective functioning of the (buried) infrastructure systems
  That are – resilient (to contextual change), unnoticed, never ending or disrupted
  And which – augment ecological ecosystem services (hence the ‘thriving planet’)
  … health & wellbeing, comfort, quality of life, a thriving planet , …
  … so how should we decide on how to carry out streetworks ?

## Slide 16: Design Options for Street Works
There are four essential design options:
  Trenching (or open-cut excavations)
  Routinely used – socially intrusive , occupies much road space, highly disruptive
  Minimum Dig Technologies
  ‘Keyhole surgery’ – downhole tools, vacuum excavation, (much) less disruptive
  Trenchless Technologies
  Pipe repair, relining, refurbishment / upgrading / upsizing, new installations
  Mature technologies – cater for all pipeline needs, small to zero disruption
  Next-Generation Robotics
  Autonomous inspection and repair – zero disruption, goes unnoticed

## Slide 17: Trenchless Technology Design Options
A screenshot from the International Society for Trenchless Technology website:
11 generic options for new installation
25 generic options for rehabilitation
49 generic options for pipeline investigation and assessment
Each links to detailed descriptions and practical guidance
… all tried and tested

## Slide 18: Pipebots
Pipebots is a 6-year programme aiming to develop swarms of small robots to work
autonomously and cooperatively
… it seeks to transform buried pipe asset management from reactive to proactive

## Slide 19: Pipebots – A Sprint Bot Approach (for Pipelines)

## Slide 20
www.ukstt.org.uk
NO-DIG LIVE 2024
Pipebots – Ultrasonic Sensing

## Slide 21: Pipebots – Trialling of Sensors

## Slide 22
Pipebots – Trialling of Sensors

## Slide 23
Pipebots – Trialling of Sensors

## Slide 24: Robotics – Autonomy (Navigation)

## Slide 25
Pipebots – Field Testing

## Slide 26: Pipebots – Timeline
Sensing
Navigation and mapping
Communication
Data analytics
Control
Grant
started
Joey
Sprintbot
Kanga
Moving towards commercial robotics
Launch
event
Technology adoption
November
2019
May
2024
January
2024
December
2020
March
2019
September
2021
June
2023
21.02.20
Trademark
underpinning science – 96 research papers
Skatebot Mk1

## Slide 27: National Buried Infrastructure Facility
A facility for testing buried pipes and tunnels at or near full scale

## Slide 28: National Buried Infrastructure Facility

## Slide 29: National Buried Infrastructure Facility

## Slide 30: National Buried Infrastructure Facility

## Slide 31: Conclusions
  Our streets are inherently valuable, as is the space below them
  … social, environmental, cultural value – all contribute to prosperity (economic value)
  We should engineer to yield greatest value now, and protect it for future generations
  Subsurface engineering is an inherently complex process, needing a ‘systems approach’
  … allows full identification of beneficial outcomes and de-risks the ‘system intervention’
  Treating the ground as an infrastructure in its own right changes perceptions
  The National Underground Assets Register has pioneered data sharing in the UK
  Trenchless Technologies, harnessing next-generation robotics, must replace trenching
  … which is unsustainable, in every sense of the word
  Research, development and (controlled) trialling will enable the 2075 transformation

## Slide 32: UK Research Facilities and Programmes
National Buried Infrastructure Facility University of Birmingham
Urban Observatory University of Birmingham
Lead Partner, PLEXUS University of Birmingham
Fire and Impact Laboratory for Resilient Infrastructure Materials University of Manchester
Urban Observatory University of Manchester
Bristol Infrastructure Collaboratory University of Bristol
National Soil-Foundation-Structure Interaction (SoFSI) Facility University of Bristol
Data and Analytics Facility for National Infrastructure (DAFNI) Rutherford Appleton Laboratory, Harwell
National Infrastructure Laboratory University of Southampton
UKCRIC Convenor University of Southampton
Advanced Infrastructure Materials Laboratory
Imperial College London
Person-Environment-Activity Research Laboratory (PEARL) University College London (UCL)
Lead Partner, UKCRIC Coordination Node (UCL)
National Research Facility for Water and Wastewater Treatment Cranfield University
Breakthrough Innovation Hub Cranfield University
Urban Observatory Cranfield University
National Research Facility for Infrastructure Sensing University of Cambridge
National Facility for Infrastructure Construction Loughborough University
Lead Partner, Centre for Postdoctoral Development (C-DICE) Loughborough University
Urban Flows Observatory University of Sheffield
National Distributed Water Infrastructure Facility University of Sheffield
Centre for Infrastructure Materials University of Leeds
Urban Observatory Newcastle University
National Green Infrastructure Facility, Urban Water Infrastructure Facilities Newcastle University
Lead Partner, City Observatory Research platfOrm for iNnovation and Analytics (CORONA) Newcastle University
Centre for Future Infrastructure University of Edinburgh
Flowave University of Edinburgh
National Robotarium Heriot-Watt University
c.d.f.rogers@bham.ac.uk